Dau Tieng Dam

Dau Tieng main dam  crest & reservoir.

EE

Location

Main earthfill Dau Tieng Dam is on the Sai Gon River in Tay Ninh Province, 70 km to the Ho Chi Minh City. The Dau Tieng Reservoir covers a ground surface in  Tay Ninh & Binh Duong Provinces.

Chief Objectives

-  Gravity irrigation for 93,400 ha. Water to pump irrigation for  40.000 ha.

-  Water supply for living & industrial demands of 100 mil.m3/year.

-  Flood mitigation for Saigon River downstream

- Yearly water regulation of Sai Gon river. Environmental promotion for 400,000 ha usually threatened by drought and protection of the Saigon River downstream from salinity intrusion.

- Using water surface and reservoir’s volume for fishery development.

Specifications:

- Flood design frequency: 		         P = 0.1%

- Normal water elevation:		         24.4 m

- Surcharged water elevation:	         25.1 m

- Dead water elevation:		         17.0 m

- Crest of dam elevation:		         28.0 m

- Total volume of water storage:		 1.58 bil.m3

- Water surface of  the reservoir     27,000 ha

Construction Sizes:

-   Dams

|  |  | Main Dam | Sub Dam |
| --- | --- | --- | --- |
| Height Crest length Crest width Dam volume | m km m mil.m3 | 29.0 1.1 8.0 2.0 | 13.0 26.0 6.0 11.0 |

-   Spillway

Designed discharge:  2,800 m3/s;       Size:  gates of (6m × 10m)

-    Canal system

Main canals

|  |  | “East” | “West” | Tan Hung |
| --- | --- | --- | --- | --- |
| Length Flow discharge | km m3/s | 46 64 | 39 70 | 29 12,8 |

Elementary canals with length of 3000 km.

Brief on Construction & Upgrading Process:

1976-1979 : Investigation.

18/5/1979 :  Project Approval.

28/4/1981:  Earth Breaking of Headwork & Main Canals with a part of WB ODA .

12/1/1983:  Partial Closure.

9/12/1983:  Completed Closure & Water Storage in Reservoir.

10/1/1985: Completion of Headwork, Main Canals & Partial System of   Elementary Canals.

1985-2005: Completion of  Elementary Canals.

1999-2000: Main Dam Strengthening with Added Downstream Earth Volume & Bentonite Trench.

The upgrading and modernization of Dau Tieng Hydraulic System as a component of the WB “Vietnam Water Resources Assistance Project” has been being implemented. The “Phuoc Hoa Hydraulic System Project” sponsored by the ADB is going to implementation including a barrage on the Be River to regulate the flow and transfer an excess of water to Dau Tieng Reservoir. It is expected a large “Hydraulic Dau Tieng – Phuoc Hoa System” into being in near future.

Spillway viewed downstream

# Text boxes

Bentonite trench was implemented in the main dam body

by advanced Bachy-Soletanche Group’s technology (1999)

East Sea